## Slide 1: Transition from the IGS14 to IGS20 antenna model file

## Slide 2: IGS20: Transition from IGSR3 to IGS20 ANTEX file
IGS14 -> IGSR3
  Galileo based satellite z-PCOs
  Multi-GNSS robot and chamber receiver antenna calibrations
  Include:
    Satellite antenna pattern: GPS, GLONASS and Galileo
    Receiver antenna pattern: multi-GNSS (including BeiDou and QZSS)
IGSR3 -> IGS20:
  Adapting IGSR3 satellite PCOs (constant to ITRF2014)
    estimation of satellite-wise GPS and GLONASS PCOs
    Estimation of one common offset for GPS BLOCK IIIA satellite (using updated disclosed pattern from Lockheed Martin)

## Slide 3: IGS20: Transition from IGSR3 to IGS20 ANTEX file
IGSR3 ANTEX file:
  Galileo based satellite z-PCOs
  Multi-GNSS robot and chamber receiver antenna calibrations
  Include:
    Satellite antenna pattern: GPS, GLONASS and Galileo
    Receiver antenna pattern: multi-GNSS (including BeiDou and QZSS)
IGS20:
  Adapting IGSR3 satellite PCOs
    estimation of satellite-wise GPS and GLONASS PCOs
    Estimation of one common offset for GPS BLOCK IIIA satellite (using updated disclosed pattern from Lockheed Martin)

## Slide 4: IGS20: Transition from IGSR3 to IGS20 ANTEX file
IGS20:
  Adapting IGSR3 satellite PCOs (in progress with IGS RF):
    estimation of stellate-wise GPS and GLONASS PCOs
    Estimation of one common offset for GPS BLOCK IIIA satellite (using updated disclosed pattern from Lockheed Martin)
    Estimation of one common offset for all Galileo satellite
  Update of receiver antenna pattern
    Repro3 ANTEX file using patterns from 2019
    Update of existing antenna pattern:
      Using PPP to estimate difference between old and updated pattern
      Taking the difference for the IGS20 realization into consideration (by IGS RF)
      Same approach as for IGS14 Restricting new antennas / receivers

## Slide 5: IGS20: Transition from IGSR3 to IGS20 ANTEX file
IGS20:
  Nadir angle extension for LEO
    Will be extended according to IGS14
    Should be updated (in particular BLOCK IIIA)
    PV will be revised
    The extension are not part of the “official” IGS20 and can be updated
  BeiDou / QZSS / IRNSS
    Manufacturer values
    Not part of the official IGS20 the values can be changed
    Might be needed to account for scale inconsistencies -> further investigations needed

## Slide 6: IGS20: Transition from IGSR3 to IGS20 ANTEX file
Adjust Repro3 Scale to ITRF compatible scale (by RF based on combined IGS repro product):
  GPS: re-estiamtion of PCOs
  GPS: on common correction for BLOCK IIIA: +8.9 cm
  GLONASS: re-estimation of PCOs
  Galileo: one common correction: +15.6 cm

## Slide 7: IGS20: Transition from IGSR3 to IGS20 ANTEX file
common offset
cm
cm

## Slide 8: IGS20: Transition from IGSR3 to IGS20 ANTEX file
common offset
cm
cm

## Slide 9: IGS20: Transition from IGSR3 to IGS20 ANTEX file
Comparison of preliminary DTRF2020 and ITRF 2020 solution based on CODE Repro3 solutions:
System | ITRF2020 | DTRF2020 | IGS20
GPS | + 13.2 cm | +1.3 cm | +8.9 cm (IIIA)
GLONASS | + 9.5 cm | +0.9 cm | ind.
Galileo | + 18.7 cm | +5.0 cm | +15.6 cm
System | ITRF2020 (2019) | DTRF2020 (2019)
GPS | + 11.6 cm | +1.6 cm
GLONASS | + 10.8 cm | +1.5 cm
Galileo | + 16.7 cm | +4.4 cm

## Slide 10: IGS20: Transition from IGSR3 to IGS20 ANTEX file
Comparison of preliminary DTRF2020 and ITRF 2020 solution based on CODE Repro3 solutions:
-> Origin of scale inconcisteny is unclear: combination/system/model
SVN |  | ITRF2020 | DTRF2020
74 | 1.851m | 1.964 m | 1.881 m
75 | 1.851m | 1.933 m | 1.833 m
 |  | ~ 10 cm | ~ 3 cm

## Slide 11: IGS20: Transition from IGSR3 to IGS20 ANTEX file
cm
cm
zPCO based in ITRF2020
zPCO based on DTRF2020

## Slide 12: IGS20: Transition from IGSR3 to IGS20 ANTEX file
zPCO based in ITRF2020
cm
cm
zPCO based on DTRF2020

## Slide 13: Open task
Scale inconsistency between techniques is an open question
TRF combination strategies should be further analysed
TRF-independent scale studies needed:
  E.g. Sentinel 6: GPS/Galileo, SLR, DORIS