## Slide 1: Control and Automation of Production Systems
Unit 6:
SFC Programming

## Slide 2: Index
Introduction
Basic elements
Rules of evolution
Examples
  Sequential processes
  Alternative processes
  Synchronization of processes
  Shared resources
2
Notes: Shared resource: Shared resources

## Slide 3: Introduction
Petri net:
  A directed graph that models the dynamic
  behavior of discrete event systems.
  Created by C. A. Petri in the 1960’s.
Advantages:
  Graphical description (reflecting the physical system).
  Complex automations (several inputs, outputs or statuses)
  Parallel processes.
  Easy to add modifications.
  Possibility of programmed implementation (GRAFCET: Stage transition command graphs)
Notes: Carl Adam Petri

## Slide 4: Basic elements
Petri net (Graph)
  Places
  Transitions
  Arcs
Places
  Markings
P1
VS1,VS2
Identification
for the place
Variables that
are only activated
when the place is marked
There can be more than one marking per place and several places marked at the same time

## Slide 5: Basic elements
Transitions
Arcs
  Place to transition
  Transition to place
VE1·VE2
T1
Identification
for the transition
Validation condition for the transition

## Slide 6: Petri net for an automation
Petri net
  The evolution of the automation = evolution of the markings in the places
  The automation initial state is shown in the originally marked places
  The transitions adjust the evolution of the markings from some places to other
  The automation inputs are associated to transitions
  The automation status is the combination of the marked places
  The automation outputs are associated to locations

## Slide 7: Rules of marking evolution
Validated transition
  All input places are marked
Transition pass
  The transition is validated
  The condition associated to the transition is true
Marking evolution
  All input places lose one marking
  All output places get one marking
Notes: The transition will be triggered

## Slide 8: Rules of marking evolution
P1
T1
P2
A·B
If the condition associated to T1 is valid (A·B=1) and the place P1 is marked
The transition is passed
P1
T1
P2
A·B
P1
T1
P4
A·B
P2
P3
P5
If A·B=1 and places P1,P2,P3 are marked
P1
T1
P4
A·B
P2
P3
P5
The transition is passed

## Slide 9: Example: sequential processes
Engine with run/stop push buttons
Push buttons (NO):
0: Open
1: Closed
Engine:
0: Stop
1: Run
AUTOMATION:
SEQUENTIAL SYSTEM
M
Engine
P
P1
T1
P2
M·P
T2
P
Engine
P: stop
M: running

## Slide 10: Example: sequential processes
Valve:
0: Closed
1: Open
LT:
0: Dry
1: Wet
V
PT1
PT2
AUTOMATION:
SEQUENTIAL SYSTEM
PT1
V
PT2
Hysteresis control of the level of a tank:
P1
T1
P2
PT1
T2
PT2
V

## Slide 11: SFC programming
Sequential Function Chart or GRAFCET
  Marking rules as Petri nets
Types
  Single marking (ICE 61131-3)
  Multi-marking (unseen)
Elements
  Step
  Transition
  Link
  Alternative branch
  Alternative conjunction
  Parallel branch
  Parallel conjunction
  Macro steps
  Jumps
Notes: Conjunción = conjunction /conyucshion/

## Slide 12: GRAFCET: Basic elements
Steps and markings
1
Actions
Identification
for the step
Marking:
Shows that the
step is
activated
Actions to be
performed only if
the step is
activated
Transitions
Identification
for the transition
(5)
A·B
Validation condition for the transition (input logic function)
5
Double square:
Originally
activated step

## Slide 13: SFC elements
Jumps
  Move the mark to the step that is marked by a jump label
Notes: Estos dos grafcet son equivalentes

## Slide 14: SFC elements
Alternative processes. Alternative bifurcation and conjunction.
Conditions a, b and c must be exclusive, so that only one branch can be followed in case the conditions are met simultaneously.
Notes: El de la derecha no es una bifurcación, son procesos paralelos
El de la izquierda no sé si es correcto, en teoría para estar bien estructurado las distintas ramas de una bifurcación deben volver al mismo sitio.

## Slide 15: SFC elements
Parallel processes. Simultaneous bifurcation and conjunction.
Condition “a” is the initial condition for the three processes to be started simultaneously
S_5_14, s_5_15, s_5_16 and condition “e” must be activated so they can pass to s_5_17
It is normal to include steps with no-effect at the end of the parallel processes in order to synchronize their final objective. The fastest processes wait for the slowest ones.
Notes: El de la derecha no es una bifurcación, son procesos paralelos
El de la izquierda no sé si es correcto, en teoría para estar bien estructurado las distintas ramas de una bifurcación deben volver al mismo sitio.

## Slide 16: Example
Engine with run/stop push buttons
Push buttons (NO):
0: Open
1: Closed
P: stop
M: running
Engine:
0: Stop
1: Run
1
0
Engine
(1)
(2)
AUTOMATION:
SEQUENTIAL SYSTEM
M
Engine
P
P1
T1
P2
M·P
T2
P
Engine

## Slide 17: Example
Valve:
0: Closed
1: Open
LT:
0: Dry
1: Wet
V
PT1
PT2
AUTOMATION:
SEQUENTIAL SYSTEM
PT1
V
PT2
Level of a tank:
1
0
V
(1)
(2)
P1
T1
P2
PT1
T2
PT2
V

## Slide 18: Exercise
Transport wagon:
V: Valve
MI : left motor
MD: right motor
VV: wagon unloading
LTH: high level sensor in wagon
LTL: low level sensor in wagon
FCD: end of stroke right
FCI: end of stroke left
P: Switch
V
FCI
FCD
MD
MI
P
Control objective:
Load the wagon, unload in the furnace and return

## Slide 19: Petri net
P
V
LTH
MD
FCD
VV
LTL
MI
FCI
P: Switch
LTH: Upper level sensor of the wagon
LTL: Lower level sensor of the wagon
FCI: End of stroke on left side of the track
FCD: End of stroke on right side of the track
V
FCI
FCD
MD
MI
P
Notes: Hacer el grafcet en la pizarra o Simulación con el CODESYS
En pizarra, no hay simulación para este ejemplo. EL de la traspa31 no es el mismo.

## Slide 20: Example: alternative processes
Engine with push buttons for turning in different directions and stop
AUTOMATION:
SEQUENTIAL SYSTEM
GD
MI
P
GI
MD
P: stop
GD: Push button, turn right
GI: Push button, turn left
MI: Engine turning left
MD: Engine turning right

## Slide 21: Example: alternative processes
Engine with push buttons for turning in different directions and stop
P: stop
GD: Push button, turn right
GI: Push button, turn left
MI: Engine turning left
MD: Engine turning right
AUTOMATION:
SEQUENTIAL SYSTEM
GD
MI
P
GI
MD
1
0
MI
(1)
2
MD
(2)
(3)
(4)

## Slide 22: Example: synchronization
P: Switch
Load independent wagons which are synchronized when unloading
ESR1
V1
ESLI1
RM1
LM1
S1
V: Valve
V2
ESL2
MD2
MI2
S2
ESR2
LTH: high level sensor in wagon
LTL: low level sensor in wagon
FCD: end of stroke right
FCI: end of stroke left
MI : motor left
MD: motor right
VV: wagon unloading

## Slide 23: Petri net
P1
V1
LTH1
MI1
FCD1
VV1
LTL1
MD1
FCI1
P2
V2
LTH2
MI2
FCD2
VV2
LTL2
FCI2
MD2
This net have to be modified in order to be implemented as an SFC code.
This will be shown later on the unit
You can find the animation for this system in the file:
Sincro_vagonetas_anim
Notes: NO hacemos el grafcet, se hará cuando se vean subsistemas

## Slide 24: Exercise
ONE SINGLE
SWITCH
P: Switch
Load independent wagons which are synchronized when unloading
FCD1
V1
FCI1
MD1
MI1
P
V: Valve
V2
FCI2
MD2
MI2
FCD2
LTH: high level sensor in wagon
LTL: low level sensor in wagon
FCD: end of stroke right
FCI: end of stroke left
MI : left motor
MD: right motor
VV: Wagon drain valve

## Slide 25: Petri net
LTH2
P
V1
LTH1
MI1
FCD1
VV1
LTL1
MD1
FCI1
V2
MI2
FCD2
VV2
LTL2
FCI2
MD2

## Slide 26: CRAFCET
V1
LTH1
FCD1
MD1
P
V2
LTH2
FCD2
MD2
VV1
LTL1
FCI1
MI1
1
VV2
LTL2
FCI2
MI2
1

## Slide 27: Example: shared resource
P: Switch
V1
Transport wagon with a common track section:
FCI1
FCD1
MD1
MI1
V: Valve
V2
FCI2
MD2
MI2
FCD2
FCT
FCD: end of stroke right
FCI: end of stroke left
FCT : end of stroke of the tank
AG=1
AG=0
AG: Track points
P1
P2
LTH: high level sensor in wagon
LTL: low level sensor in wagon
Notes: Shared resource

## Slide 28: Petri net
MI1,AG
P1
V1
LTH1
MD1
FCD1
MD1,AG
FCT
VV1
LTL1
FCD1
MI1
FCI1
P2
V2
LTH2
MD2
FCD2
MD2
FCT
VV2
LTL2
FCD2
MI2
FCI2
MI2
This net have to be modified in order to be implemented as an SFC code.
This will be shown later on the unit
Notes: NO se hace el grafcet porque se ve al final del tema

## Slide 29: Transition timing
Aim at validating a transition with a time condition.
Example:
  Keeping a step active for 3 seconds after it is triggered.
Performed with timers, equipped in the PLC.
There are several types; we will use the level-activated ones.
They are treated as an external device to the automation, with an activation signal and an end of timer signal

## Slide 30: Transition timing
L1
T1
L2
b
T2
FT
f
L3
L4
T3
FT
AT
AT
COMBINATIONAL
ES1
SS1
ESN
SS2
TIMER
10 seconds
AT
FT
AUTOMATION
AT
FT
L2
10 s
L4
10 s
Notes: Etapa L2 activa AT y 10s después se activa FT q valida la transición a la siguiente etapa

## Slide 31: Example
P: Running button
V
Transport wagon:
FCI
FCD
MD
MI
P
V: Valve
MD: right motor
MI : left motor
FCD: end of stroke right
FCI: end of stroke left
VV: Draining valve
The filling time is 180 seconds, and the draining time is 30 seconds

## Slide 32: Example
P
V , AT180
FT180
MD
FCD
VV , AT30
FT30
MI
FCI
The timers will programmed in LD in a different POU.
Notes: Hacer en grafcet, Ya sea en pizarra o en el programa

## Slide 33: Counters
They are variables used to store the amount of times that a sequence has been executed.
Equipped in the PLC.
They are considered as an external device to the automation, with increment, decrement, reset input signal, and output signal.
The counter is incremented or decremented by a rising edge of the input signal
COMBINATIONAL
ES1
SS1
ESN
SS2
COUNTER
IC
C=0
AUTOMATION
DC
RS
C>100

## Slide 34: Types of counters
CTD: Down counter
CD: Counter decrement
LD: Load data
PV: Preset value
Q: Output
CV: Count value
Functioning:
LD signal sets 'cv' to the value in 'pv' when high
CD signal decrements the counter by 1 on a rising edge.
PV. Preset value for the counter
If CV ≤ 0, the exit Q becomes "1".
Notes: EN and Eno are used in fuctions block diagrams

## Slide 35: Types of counters
CTU: Up counter
CU: Counter up
R: Reset
PV: Preset value
Q: Output
CV: Count value
Functioning:
CU signal increments the counter by 1 on a rising edge.
R signal sets 'cv' to 0 when high.
PV. Preset value for the counter
If CV ≥ PV, the exit Q becomes "1".

## Slide 36: Types of counters
CTUD: Up/down counter
CU: Count up
CD: Count down
R: Reset
LD: Load data
PV: Preset value
QU: Output up
QD: Outout down
CV: Count value
Functioning:
CU signal increments the counter by 1 on a rising edge. CD signal decrements the counter by 1 on a rising edge.
R signal sets 'cv' to 0 when high. LD signal sets 'cv' to the value in 'pv' when high.
PV. Preset value for the counter
If CV ≥ PV, the exit QU becomes "1". If CV ≤ 0, the exit QD becomes "1".

## Slide 37: Example
P: Running button
V
Transport wagon:
FCI
FCD
MD
MI
V: Valve
MD: right motor
MI : left motor
FCD: end of stroke right
FCI: end of stroke left
P
The filling time is 180 seconds, and the draining time is 30 seconds
Every time the running button is pressed, the process is executed 7 times
VV: Draining valve

## Slide 38: Example
P
V , AT180
FT180
MD
FCD
VV , AT30
FT30
MI,IC
FCI·CQ
FCI·CQ
RESET
Check example: vagoneta_temp_traspa_31.pro

## Slide 39: Subsystem division
For the implementation of complex automations, it is useful to divide it into subsystems
  Easy programming and debugging
  Easy maintenance
Each subsystem corresponds to one program-type POU, which is executed in a specified order
Subsystems exchange information through internal variables defined by the user (as input or output variables) or through global variables.
Notes: ¿Y var input y Var output? No se podían usar por otras POUS poniendo el nombre de la POU.variable?

## Slide 40: Subsystem division
For each subsystem, it is necessary to define
  Inputs
    Automation inputs
    Automation outputs managed by other subsystems
    Internal variables managed by other subsystems
  Outputs
    Automation outputs
    Internal variables
Several subsystems cannot share output signals
  Multiple assignment problem!

## Slide 41: Exercise
ONE SINGLE
SWITCH
P: Switch
Load independent wagons which are synchronized when unloading
FCD1
V1
FCI1
MD1
MI1
P
V: Valve
V2
FCI2
MD2
MI2
FCD2
LTH: high level sensor in wagon
LTL: low level sensor in wagon
FCD: end of stroke right
FCI: end of stroke left
MI : left motor
MD: right motor
VV: wagon unloading

## Slide 42: Modular Petri net
LTH2
P
V1
LTH1
MI1
FCD1
VV1
LTL1
MD1
FCI1
V2
MI2
FCD2
VV2
LTL2
FCI2
MD2
P
P
LTH1
MI1
FCD1
VV1
LTL1
MD1
FCI1
V1
FTD1
FTD1·FTD2
FTI1
FTI1·FTI2
LTH2
V2
MI2
FCD2
VV2
LTL2
FCI2
MD2
FTD2
FTD1·FTD2
FTI2
FTI1·FTI2

## Slide 43: Modular Petri net
Internal signals
  FTD1,FTD2
  FTI1, FTI2
P
P
LTH1
MI1
FCD1
VV1
LTL1
MD1
FCI1
V1
FTD1
FTD1·FTD2
FTI1
FTI1·FTI2
LTH2
V2
MI2
FCD2
VV2
LTL2
FCI2
MD2
FTD2
FTD1·FTD2
FTI2
FTI1·FTI2
VAR_GLOBAL
FTD1:BOOL;
FTD2:BOOL;
FTI1:BOOL;
FTI2:BOOL;
END_VAR
Notes: In this particular case, sensors could be used
Signal synchronization is more robust and versatile

## Slide 44: Red de Petri modular
P
P
LTH1
MI1
FCD1
VV1
LTL1
MD1
FCI1
V1
FTD1
FTD1·FTD2
FTI1
FTI1·FTI2
LTH2
V2
MI2
FCD2
VV2
LTL2
FCI2
MD2
FTD2
FTD1·FTD2
FTI2
FTI1·FTI2
V1
VV1
MD1
MI1
MD1
FTD1
FTI1
LTH1
LTL1
FCD1
FCI1
FTD2
FTI2
P
VAGON 1
V2
VV2
MD2
MI2
MD2
FTD2
FTI2
LTH2
LTL2
FCD2
FCI2
FTD1
FTI1
P
VAGON 2
Notes: En este caso particular podría usarse los sensores
La sincronización por señales es más robusta y versátil

## Slide 45: Example: shared resource
P: Switch
V1
Transport wagon with a common track section:
FCI1
FCD1
MD1
MI1
V: Valve
V2
FCI2
MD2
MI2
FCD2
FCT
FCD: end of stroke right
FCI: end of stroke left
FCT : end of stroke of the tank
AG=1
AG=0
AG: Track points
P1
P2

## Slide 46: Modular Petri net
MI1,AG
P1
V1
LTH1
MD1
FCD1
MD1
FCT
VV1
LTL1
FCD1
MI1
FCI1
P2
V2
LTH2
MD2
FCD2
MD2
FCT
VV2
LTL2
FCD2
MI2
FCI2
MI2

## Slide 47: Modular Petri net
MI1,AG
P1
V1
LTH1
MD1
FCD1
MD1
FCT
VV1
LTL1
FCD1
MI1
FCI1
P2
V2
LTH2
MD2
FCD2
MD2
FCT
VV2
LTL2
FCD2
MI2
FCI2
MI2
OCUP1
OCUP2
OCUP2
OCUP1
VAR_GLOBAL
OCUP1:BOOL;
OCUP2:BOOL;
END_VAR
V1
VV1
MD1
MI1
MD1
OCUP1
LTH1
LTL1
FCD1
FCI1
OCUP2
P1
WAGON 1
V2
VV2
MD2
MI2
MD2
OCUP2
LTH2
LTL2
FCD2
FCI2
OCUP1
P2
WAGON 2

## Slide 48: Modular Petri net
MI1,AG
P1
V1
LTH1
MD1
FCD1
MD1
FCT
VV1
LTL1
FCD1
MI1
FCI1
P2
V2
LTH2
MD2
FCD2
MD2
FCT
VV2
LTL2
FCD2
MI2
FCI2
MI2
OCUP1
OCUP2
FREE
FREE
VAR_GLOBAL
OCUP1:BOOL;
OCUP2:BOOL;
LIBRE:BOOL;
END_VAR
V1
VV1
MD1
MI1
MD1
OCUP1
LTH1
LTL1
FCD1
FCI1
FREE
P1
WAGON 1
V2
VV2
MD2
MI2
MD2
OCUP2
LTH2
LTL2
FCD2
FCI2
FREE
P2
WAGON 2
Notes: Alternative solution

## Slide 49: Modular Petri net
FREE
OCUP1
OCUP2
RESOURCE
FREE
OCUP1
OCUP2
Implementation in LD
free
free
OCUP1
OCUP1
OCUP2
OCUP2
Notes: Lo importante es recalcar que se puede usar cualquier lenguaje
Rehacer el ejemplo para que el grafcet coincida con las variables
Hacemos en el centro de cálculo los siguientes ejercicios
1º bagonetas con sincronización en la descarga
2º de la traspa 31 con temporizadores y contadores
3º el de los depósitos
4º el de los AGV como ejemplo de recurso compartido