## Slide 1: Modeling LLNL’s Pulsed Neutron Die Away (PNDA) Benchmarks
Objective
Model the PNDA benchmark setup in Mercury
Conclusions
A Mercury model for the PNDA experiments produced comparable results to MCNP
Background
The PNDA benchmarks are meant to assess Thermal Neutron Scattering Law data (TNSL), S(,)
A pulse of neutrons scatters in a cylinder of material
  After the pulse ends, an exponential decay of the neutron population can be fit for
Future Work
Discrepancies with several TNSL materials need further investigation
Updates to the GNDS data format at LLNL are still ongoing
  Isotopic abundance capabilities have been added so far
Daniel Siefman at LLNL is performing more experiments with better characterization
Experiments with more materials have been proposed
Acknowledgements
This work was supported by the Center for Exascale Monte-Carlo Neutron Transport (CEMeNT) a PSAAP-III project funded by the Department of Energy, grant number DE-NA003967.
Jordan Northrop, Scott McKinley, Ali Dreyfuss, Marie-Anne Descalle
Lawrence Livermore National Laboratory (LLNL)
Experiment Comparison
Results
GNDS Issues
TNSL Data
A Mercury model and a preliminary Ardra model were produced
The die away curves for each of the codes aligned well
For well defined TNSL materials (H2O, HDPE), the alpha values were typically less than 1% apart
Alpha values produced were generally well within 20% of the experiment values
The experiments need better characterization (density etc.)
Certain materials known to cause issues before [1] showed small discrepancies between MCNP and Mercury
A map file issue prevented proper implementation of elements with multiple natural isotopes as well as a couple specific TNSL materials
TNSL has higher impact
TNSL has higher impact
depends on an absorption term, the geometry, and a diffusion coefficient influenced by TNSL
References
[1] A. C. Dreyfuss, B. R. Beck, P. N. Brown, C. M. Mattoon and M. S. McKinley, “TNSL Overview”, https://www.osti.gov/servlets/purl/ 1828675